## Slide 1: FLEXFEC SDP
Ali C Begen
Varun Singh
Mo Zanaty
MMUSIC
IETF 91
draft-singh-payload-rtp-1d2d-parity-scheme-00

## Slide 2: Motivation
Current FEC standards lack sufficient flexibility to be usable for many use cases, including RTCWEB
RFC 2733 XOR with 24-bit mask: obsoleted by 5109
RFC 5109 XOR with 48-bit mask and ULP:
  SSRC multiplexing not supported
    draft-lennox-payload-ulp-ssrc-mux proposes a=ssrc-group:FEC
  48-bit mask insufficient for interleaved FEC to recover from burst loss, and requires >2% FEC
RFC 6015 XOR with fixed 1D interleaved FEC:
  Non-standard RTP header prevents general use
  Fixed parameters not suited for adaptive real-time cases
RFC 6682 Raptor FEC: IPR declarations exist
RFC 6865 Reed-Solomon FEC: no RTP format

## Slide 3: Proposed Solution
New flexible FEC payload format ‘FLEXFEC’
Flexibility to use different multiplexing:
  SSRC multiplexing (e.g. BUNDLE, Unified Plan)
  RTP session multiplexing (e.g. multicast, legacy SIP)
  PT multiplexing within the same RTP stream
  RED multiplexing within the same RTP packet
Flexibility for sender to adapt FEC scheme based on dynamic network conditions (e.g. RTCP)
16, 48 or 112-bit mask for irregular FEC patterns
  112-bit mask allows larger source blocks and <1% FEC
Virtual bit mask for larger, regular FEC patterns up to:
  255 non-interleaved (1D row) source packets, or
  255x255 interleaved (2D column*row) source packets

## Slide 4: SDP using PT association
a=rtpmap:96 VP8/90000
a=rtpmap:97 H264/90000
a=rtpmap:98 FLEXFEC/90000
a=fmtp:98 apt=96,97; code=xor; repair-window=200ms
apt associates the Redundant Stream packets with the source Encoded Stream packets. (Similar to RTX)
repair-window specifies how long the receiver can wait for repair packets, in units of ms or us.
code is an optional parameter for future extensibility to more FEC codes.
  default is xor if omitted

## Slide 5: SDP using SSRC association
a=rtpmap:96 VP8/90000
a=rtpmap:97 H264/90000
a=rtpmap:98 FLEXFEC/90000
a=fmtp:98 code=xor; repair-window=200ms
a=ssrc:1234
a=ssrc:5678
a=ssrc-group:FEC-FR 1234 5678
ssrc-group associates the Redundant Stream (SSRC 5678) with the source Encoded Stream (SSRC 1234).

## Slide 6: Next steps
Agree in MMUSIC on multiplexing and binding source and repair streams in SDP
Adoption as PAYLOAD WG-item